## Slide 1: Synoptic Observations

## Slide 2: Synoptic Global Scale Mesoscale Microscale
Scale of Motion
Largest
Smallest

## Slide 4
Pressure Trend
Relative Humidity
Visibility
Temperature
Dew Point
Wind Direction
Wind Speed
Precipitation
Barometric Pressure
Cloud Cover
Past Weather
Present Weather

## Slide 5
Station Model (Model)
Ship reports (Numbers)

## Slide 6: Ship Report / Ship Synoptic Code Coded report of surface observation from a sea station

## Slide 7
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
Examples of Ship Reports:
BBXX
SHIP 24121 99122 71353 31475
82706 10252 20225 40061 55008 76062 83223 91312 22242 00234 20805 31215 40806 51005 62052 80122 ICE 23223

## Slide 8
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
Identifier for Ship weather report
BBXX :
Surface report from Coastal Station | AAXX
Surface report from Ship | BBXX

## Slide 9
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
Call sign of the Ship
BRAVO :

## Slide 10
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
20: Day of the month (20th)
20 12 3 :
YYGGiw
12: Time of Obeservation in UTC (4 PM Local Time)
3: wind speed type / unit (table1)
Code Figure | Iw indicator | 
0 | Wind Speed Estimated | m/s
1 | Wind Speed from anemometer | m/s
3 | Wind Speed Estimated | knots
4 | Wind Speed from anemometer | knots

## Slide 11
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
20: Day of the month (20th)
20 12 3 :
YYGGiw
12: Time of Obeservation in UTC (4 PM Local Time)
3: Wind Speed is estimated / knots

## Slide 12
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
99: Indicator for sea station position groups (Latitude)
99 252 :
99LaLaLa
252 : Degrees and tenth (25.2°)

## Slide 13
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
1: Quadrant of the globe
1 0595 :
QcLoLoLo
0595: Longitude, Degrees and tenth (59.5°)

## Slide 14
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
25.2° N
Latitude:
Longitude:
59.5° E

## Slide 15
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
4 : Indicator figure for precipitation group (Table 3)
1 : Type of station and present and past weather indicator (Table 4)
4 : height of the base of the lowest cloud (Table5)
94 : horizontal visibility (Table6)
4 1 4 94 :
iRiXhVV
1 | Precipitation group Included
2 | Precipitation group Included
3 | Precipitation group No Precipitation
4 | Precipitation group Not available
Not Available
Manned/Included
1 | Manned / Included
2 | Manned / Omitted / No Phenome
3 | Manned / Omitted / Not Available
4 | Auto / Included
5 | Auto / Omitted / No Phenome
6 | Auto / Omitted / Not Available
7 | Auto / Included
1000 to 2000 ft
1 km

## Slide 16
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
8 : Total cloud amount (Table 7)
8 14 12:
Nddff
14 : Wind Direction tenth of degrees
12: Wind Speed (12 knots)
Overcast
140°, SE

## Slide 17
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
1 : Group indicator for air temperature
1 0 285:
1snTTT
0 : Temperature sign is + (if 1 Temperature sign is - )
285 : Air Temperature is 28.5 °C

## Slide 18
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
2snTdTdTd
2 : Group indicator for Dew Point Temp
2 0 269:
0 : Temperature sign is + (if 1 Temperature sign is - )
269 : Air Temperature is 26.9 °C

## Slide 19
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
4 : Group indicator for MSL Pressure
4 0100:
4PPPP
0100 : MSL Pressure of 1010.0 hPa

## Slide 20
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
5 : Group indicator for Pressure change
5 3 012:
5appp
3 : Code Identifier (Table 11)

## Slide 21
Table 11

## Slide 22
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
5 : Group indicator for Pressure change
5 3 012:
5appp
3 : Code Identifier (Table 11) (Pressure increasing)
012 : Pressure change of 0.12 hPa in the last three hours

## Slide 23
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
7 : Weather Type Indicator
7 95 86:
7wwW1W2
95 : Current weather
86 : Past weather
Thunderstorm and drizzle
Shower and Rain

## Slide 24
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
8 : Cloud Indicator
8587/:
8NhOrCLCMCH
5 : Amount of Low or medium Cloud 5/8
8 : low cloud type (Table 14)
7 : medium cloud type (Table 15)
/ : High cloud type (Table 16)

## Slide 25
Table 14

## Slide 26
Table 14 conti.

## Slide 27
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8587/ 22265 00280 20405 31705 40506 50407=
8 : Cloud Indicator
8587/:
8NhOrCLCMCH
5 : Amount of Low or medium Cloud 5/8
8 : low cloud type (Table 14)
7 : medium cloud type (Table 15)
/ : High cloud type (Table 16)
Cumulus and Stratocumulus

## Slide 28
Table 15

## Slide 29
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
8 : Cloud Indicator
8597/:
8NhOrCLCMCH
5 : Amount of Low or medium Cloud 5/8
9 : cumulonimbus
7 : Altocumulus
/ : High clouds type (Table 16)

## Slide 30
Table 16

## Slide 31
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
8 : Cloud Indicator
8597/:
8NhOrCLCMCH
5 : Amount of Low or medium Cloud 5/8
9 : cumulonimbus
7 : Altocumulus
/ : invisible

## Slide 32
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
222 : Section indicator of maritime data
222 6 5:
222DsVs
6 : Direction where the ship is moving
5 : Ship average speed last 3 hours
Ship is moving West in the last 3 hours
21 to 25 knots

## Slide 33
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
0 : group indicator of SST
0 0 280:
OSsTwTwTw
0 : Temperature sign is + (if 1 Temperature sign is - )
280 : SST is 28.0 °C

## Slide 34
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
2 : group indicator for wind waves
20405:
2PwPwHwHw
04 : Period of wind wave (4 seconds)
05 : Height of wind wave in units of half meters
(2.5 m/s)

## Slide 35
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705 40506 50407=
3 : group indicator for swell direction
31705:
3dwdw1//
17 : Direction of first Swell
05 : Direction of Second Swell
170° , SE
50° , NE

## Slide 36
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705
40506 50407=
4 : indicator for period and height of first swell group.
40506:
4Pw1Pw1Hw1Hw1
05 : period of first swell (05 sec).
06 : height of first swell in unit of half meter. (06 X 0.5=3 m)

## Slide 37
BBXX
BRAVO 20123 99252 10595 41494
81412 10285 20269 40100 53012 79586 8597/ 22265 00280 20405 31705
40506 50407=
5 : indicator for period and height of nd swell group.
5 04 07:
5Pw2Pw2Hw2Hw2
04 : period of second swell (04 sec)
07 : height of second swell in unit of half meter
(07 X 0.5=3.5 meters)

## Slide 38: METAR

## Slide 39: METAR OOMS 172250Z 22003KT 190V250 CAVOK 24/14 Q1009 NOSIG
OOMS: Muscat International Airport
172250Z :
17 : date of the month
2250Z: Time of observation 22:50 UTC

## Slide 40
METAR OOMS 172250Z 22003KT 190V250 CAVOK 24/14 Q1009 NOSIG
22003KT
220: Wind Direction
03KT: Wind speed is 3 knots
190V250
Wind Direction is varying from 190° to 250°

## Slide 41
METAR OOMS 172250Z 22003KT 190V250 CAVOK 24/14 Q1009 NOSIG
CAVOK : Clouds and Visibility is OK
* Visibility is 10km or more.
* no cloud below 5000 feet
* No significant weather at or in the vicinity of the aerodrome.

## Slide 42
METAR OOMS 172250Z 22003KT 190V250 CAVOK 24/14 Q1009 NOSIG
24 : Temperature
14 : Dew point

## Slide 43
METAR OOMS 172250Z 22003KT 190V250 CAVOK 24/14 Q1009 NOSIG
Q1009 : Pressure 1009 mb
NOSIG: No significant change expected

## Slide 44: Station Plot Station Model

## Slide 45: Station Model / Surface Plot Simple symbols to display large amounts of meteorological information in a small area.

## Slide 46: Synoptic Observations: Surface 850 mb 700 mb 500 mb 300 mb Upper Air Observations

## Slide 48: Manual Observation Automatic Observation

## Slide 49
23
55
18
871
090703
8/4
25
10603
Notes: time between successive occurrences of the same state

## Slide 50: Cloud Cover Overcast

## Slide 51: Wind Direction North West From

## Slide 52: Wind Speed 18-22 Knots 9-11 m/s

## Slide 53: Air Temperature 23 °C
23

## Slide 54: Current Weather Moderate Rain
23
Notes: Rain-cloud cover

## Slide 55: Visibility 6 km
23
56
In either meters or kilometres
Visibilities below five kilometres are recorded to the nearest 100 metres
Visibilities above five kilometres are given to the nearest kilometre
(0-50)--------(0.0-5.0 km)
(56-80)------(06-30 km)
(81-88)------(35-70 km)

## Slide 57: Dew Point 18 °C
23
56
18

## Slide 58: High Cloud Type
23
56
18

## Slide 59: Medium Cloud Type
23
56
18

## Slide 60: Low Cloud Type
23
56
18

## Slide 61: Low Cloud Cover/ Hight
23
56
18
8/4

## Slide 62: Pressure 987.1 mb
23
56
18
Pressure is recorded in millibars and tenths and the last three digits are plotted
871
(0-4)-------- Add 10 and point
(5-9)------ Add 9 and point
8/4

## Slide 63: Pressure Tendency
23
56
18
871
8/4

## Slide 64: Past Weather Or Cloud Cover
23
56
18
871
8/4

## Slide 65: Sea Surface Temperature 25 °C
23
56
18
871
25
8/4

## Slide 66: Wave Information 1: Group Identifier (Bouey) 06: Wave Period 6 Seconds 03: Wave Height 3 Half meters 2: Group Identifier (Ship)
23
56
18
871
8/4
25
10603

## Slide 67: Swell Information 09: Swell Direction (From 90°) 07: Swell Period 7 Seconds 03: Swell Height 3 Half meters
23
56
18
871
090703
8/4
25
10603
Notes: time between successive occurrences of the same state

## Slide 68
23
56
18
871
090703
8/4
25
10603
Notes: time between successive occurrences of the same state

## Slide 69: Thank You
Got questions?