## Slide 1: Introduction to Earth Observing Satellites
Dr Humaid AlBadi
3 September 2023

## Slide 2
What is a satellite?
Satellite: In astronomical terms, a satellite is a celestial body that orbits around a planet.
Example: The moon is a satellite of Earth.
In aerospace terms, a satellite is a space vehicle launched by humans and orbits around Earth or another celestial body.
Satellites: Definition

## Slide 3
How do satellites observe the Earth?
Via radiometers (Imager, Sounder, Receiver) that measure radiation flux (Power).
> Earth Observation Satellites usually carry many radiometers
How do satellites observe the Earth?
What is the difference between satellite imagers, sounders, and receivers?
Sounders can be passive or active, collect broad- and narrow-band radiance and the viewing geometry is either nadir or limb-staring.
An imager radiometer is a passive nadir broadband sounder. A receiver is a radiometer for radar backscattering.

## Slide 4
Spectral signature of an object is the variation of reflectance or emittance of the object with respect to wavelengths.
Spectral signature is the main principle behind satellite remote sensing applications
Spectral Signature
How do satellites observe the Earth?

## Slide 5
The wavelength of an object’s peak emission (λm) is inversely proportional to the temperature of the object:
λm
Another key physical idea behind remote sensing applications
How do satellites observe the Earth?
The wavelength of an object’s peak emission (λm) correlates with its temperature

## Slide 6
Digital Image resolution number of Pixels
How do satellites observe the Earth?
Satellite Sensor Resolutions

## Slide 7
Spatial - the size of the pixel represented in the field of view,
e.g. 10 x 10 m.
Satellite Sensor Resolutions
How do satellites observe the Earth?
1 Meter Resolution | 10 Meter Resolution | 30 Meter Resolution

## Slide 8
Spectral - the size of spectral regions. The shorter, the higher the spectral resolution.
How do satellites observe the Earth?
Satellite Sensor Resolutions
3-band image with Red, Green, and Blue
1 band image with just "gray scale" data.
Notes: https://www.researchgate.net/figure/Relation-of-spatial-temporal-and-spectral-resolution-of-satellite-images-106_fig1_323984631

## Slide 9
Radiometric resolution - the sensitivity of detectors to small differences in electromagnetic energy (relates to how much information is perceived by a satellite’s sensor).
Satellite Resolutions
How do satellites observe the Earth?
Bit | Shades of Grey
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256

## Slide 10
• Temporal - how often the sensor acquires data, e.g., every 10 minutes.
Satellite Resolutions
How do satellites observe the Earth?
Instrument | Spatial Res. | Temporal Res. | Swath
Sentinal-1 | 5 m | 12 days | 400 km
MODIS | 250 m | 12 hours | 2300 km
VIIRS | 371 m | 12 hours | 3000 km
SEVIRI | 1-3 km | 15 minutes | 

## Slide 11
How do satellites observe the Earth?
Satellite Sensor Resolutions
The relation between the swath, the spatial, temporal, and spectral resolution of satellite sensors.
Notes: https://www.researchgate.net/figure/Relation-of-spatial-temporal-and-spectral-resolution-of-satellite-images-106_fig1_323984631

## Slide 12
How do satellites observe the Earth?
Satellite Sensor Resolutions
The relation between the swath, the spatial, temporal, and spectral resolution of satellite sensors.
Notes: https://www.researchgate.net/figure/Relation-of-spatial-temporal-and-spectral-resolution-of-satellite-images-106_fig1_323984631

## Slide 13
History of Satellites

## Slide 14: History
Receiving images from Low Earth Orbiting in 1983
An Image from Current Satellite Receiving Stations
1983-08-9 11:00
History of Satellites
Satellite data at Meteorological Services

## Slide 15
The satellite concept evolution
1945 Theorist Arthur C. Clarke predicted that a satellite orbiting in equatorial orbit would look stationary if moving at a specific speed. 3 satellites in space, 120 degrees apart, can cover the whole world if placed in an orbit with a radius of approximately 42,000 km.
History of Satellites
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites

## Slide 16
1950’s and 1960’s – Putting the pieces together
1957  Sputnik-1 was the first satellite launched by the former USSR. It was used to identify the atmospheric density of various orbital layers. It provided data about radio-signal distribution in the ionosphere.
1958  First US satellite was launched (Explorer 1 )
1960  TIROS-1 was the first full-scale weather satellite, the first of a series of television Infrared Observation Satellites placed in low Earth orbit.
History of Satellites
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites

## Slide 17
1970’s – The start of the routine operational Satellites
1970  Landsat-1 was launched
1977  Meteosat-1
1979  NOAA -1
History of Satellites
2021  Landsat-9
2022  Meteosat-12
2021  NOAA-21
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites

## Slide 18
1970’s – The introduction of two key instruments to satellite remotes sensing
  1972 - Multispectral sensors, first used in Landsat-1
  1976 - Charge Couple Device Array
  It’s lightweight, low-powered and about 15 times more sensitive to light than regular photographic film.
History of Satellites
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites

## Slide 19
1980’s and 1990’s – The decades of new experimental sensors
  Satellite hyperspectral sensors that combine information from several spectral bands.
  Spaceborne radars, active microwave systems that can sense through cloud cover and without daylight, measuring the time delay between emission and return, thus establishing the location, height and scattering properties of the Earth's surface.
History of Satellites
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites

## Slide 20
The last two decades – The decades of the operational space Radars (Synthetic Aperture Radars, scatterometers and altimeters)
Satellite radar applications have now diversified considerably
Altimeters sensitive enough to measure sea-level height with a precision of several millimetres
scatterometers to measure surface roughness and wind
Interferometric imagers, which sense the superposition of different wavelengths, to monitor minute land movements.
History of Satellites
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites

## Slide 21
Example of Public EO data providers
More: Go to WMO OSCAR | List of all space agencies
Earth Observation data providers
ESA | https://earth.esa.int/eogateway/missions
Eumetsat | http://www.eumetsat.int/website/home/index.html
Copernicus-Sentinel | https://sentinel.esa.int/web/sentinel/ https://www.sentinel-hub.com/
USGS (Landsat) | http://earthexplorer.usgs.gov/
NOAA | http://www.ospo.noaa.gov/
NASA | https://earthdata.nasa.gov/earth-observation-data
Japan | http://www.eorc.jaxa.jp/en/about/distribution/index.html
China | http://www.cma.gov.cn/en
India | http://bhuvan.nrsc.gov.in/bhuvan_links.php
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites https://gisgeography.com/free-global-dem-data-sources/
https://business.esa.int/newcomers-earth-observation-guide#ref_4

## Slide 22
Examples of Global Commercial EO data providers
Earth Observation data providers
Digital Globe resellers (MAXAR) | http://www.digitalglobe.com/partners/certified-resellers
Airbus | https://www.intelligence-airbusds.com/access-to-our-products/
Deimos | https://www.deimos-imaging.com/imagery-store/
Planet Labs | https://www.planet.com
Urthecast | https://www.urthecast.com
MDA Geospatial Services | http://gs.mdacorporation.com/Partners/Partners.aspx
E-geos | http://www.e-geos.it/index.html
Satellite Imaging Corporation | http://www.satimagingcorp.com/
CGG | http://www.cgg.com/default.aspx?cid=7450
European Space Imaging | http://www.euspaceimaging.com/
Land info | http://www.landinfo.com/
Precision Hawk | https://www.precisionhawk.com/satellite
Apollo Mapping | https://apollomapping.com/
GHGSat | https://www.ghgsat.com/
Notes: https://www.americanscientist.org/article/fifty-years-of-earth-observation-satellites https://gisgeography.com/free-global-dem-data-sources/ https://business.esa.int/newcomers-earth-observation-guide#ref_4

## Slide 23
Use the Filter table on the page to answer how many operation Earth Observation Satellite?
Search for information about an Earth Observation satellite you have used before and talk about :
  Its operator
  How to get the data
  Its applications
Go to https://space.oscar.wmo.int/satellites
Practical Task 1

## Slide 24
https://space.oscar.wmo.int/satellites
Practical Task 1

## Slide 25
There are two main types of EO satellites
Geostationary (other name: Geo Synchronized)
Low Orbiting
Earth Observing Satellites: Types

## Slide 26
located over the equator at a height of 36000 km.
remain stationary with respect to the Earth's surface.
give images at a high and constant rate (good for animation).
Meteosat-8 41.5⁰ East
Geostationary Satellites

## Slide 27
Any object travelling in a circle at constant speed is always accelerating away from the centre of the circle by the centrifugal force .
Gravity keeps satellites in circular motion because it acts as a constant force opposing the direction of centrifugal
Why satellites do not fall on Earth? Why should geostationary satellites be at 36000 km?
v1
r
Geostationary Satellites

## Slide 28
In 1687 Newton published his gravitational FG force theory
where G is the universal gravitational constant, is the mass of the earth and m is the mass of the satellite.
For = 24 hours the distance is 36000 km
Why should geostationary satellites be at 36000 km?
It can be shown that r ; the distance between the earth and the satellite, can be calculated from the period of rotation around the earth
Geostationary Satellites

## Slide 29
GOES 16
(US)
(75W)
METEOSAT 11
Europe
(0)
INSAT 3DR
(India)
(74E)
ELEKTRO-L-N2 Russia
(76E)
Himawari-8
Japan
(140E)
GOES 14
(US)
(90W)
FY-2G China
(105E)
GOES 17
(US)
(104W)
METEOSAT 9 Europe (41.5E)
GOES 15
(US)
(135W)
METEOSAT 10
Europe (rapid scan)
(9.5E)
METEOSAT 9
Europe
(3.5E)
FY-4A China
(105E)
FY-2H China
(79E)
Current coverage of the WMO Integrated Global Observing System (WIGOS)
Geostationary Satellites
COMS
Korea
(128E)
Himawari-9
Japan
(140E)
Notes: Graphic on coverage by geostationary satellites.
Red satellites are not producing imagery on anything but a test status. GOES 9 and 11 are on-orbit spares.
INSAT is purple because AFWA does get the imagery, but too late to be of use for anything other than post analysis.
Elektro is yellow for it’s poor operational capability.

## Slide 30
Best Earth Observation Geostationary Satellites for West Asia Region
METEOSAT-11 and METEOSAT- 9
Geostationary Satellites

## Slide 31
Low Orbiting Satellites

## Slide 32: Features
lower altitude of 200 to 2000 km.
orbit from pole to pole in about 100 minutes.
more detailed but less frequent images.
Low Orbiting Satellites

## Slide 33
Low Orbiting Satellites
> 60º

## Slide 34
Low Orbiting Satellites

## Slide 35: MetOP Europe - EUMETSAT
IASI - Infrared Atmospheric Sounding Interferometer
MHS - Microwave Humidity Sounder
GRAS - Global Navigation Satellite System Receiver for Atmospheric Sounding
ASCAT - Advanced Scatterometer
GOME-2 - Global Ozone Monitoring Experiment-2
AMSU-A1/AMSU-A2 - Advanced Microwave Sounding Units
HIRS/4 - High-resolution Infrared Radiation Sounder
AVHRR/3 - Advanced Very High Resolution Radiometer
A-DCS - Advanced Data Collection System
SEM-2 - Space Environment Monitor
SARP-3 - Search And Rescue Processor
SARR - Search And Rescue Repeater
Spacecraft | Mission Operational Status
METOP-A | deorbited
METOP-B | AM Primary
METOP-C | PM Primary
Earth Observing Satellites: Examples

## Slide 36: The Copernicus Sentinel missions and their applications
Polar orbit for the Sentinel-1A and Sentinel- 1B satellites. Sentinel1 uses a radar imaging sensor with cloud penetration, all- weather, day-and-night conditions mission
Used for land and ocean services; oil spills, flood detection, forestry & agriculture, ground movement, icebergs, sea Ice
Sentinel-2B satellites. Equipped with a multispectral high-resolution imaging sensor
Sentinel-2
Sentinel-1
Polar orbit for the Sentinel-2A and
Applications in land monitoring; vegetation, soil, inland waters, coast, agriculture & forestry, water quality, and emergency
Also, polar orbit for the Sentinel-3A and Sentinel-3B satellites. Provided with multi-instrument for measuring sea-surface topography, surface temperature, ocean and land colour
Sentinel-3
To support ocean forecasting, environmental and climate monitoring; Water quality, sea level, altimetry, biomass
Sentinel-5P
The forerunner satellite of Sentinel-5 mission. With sensors to acquire concentrations of trace gases and aerosols
For air quality and climate analysis;
Greenhouse gases, air pollution, SO2,
CO2, aerosols, PM, CH4, formaldehyde, etc.
A radar altimeter measurement system for measuring sea-surface height and map sea-surface topography
Sentinel-6
To support oceanography, climate studies, and sea monitoring
Earth Observing Satellites: Examples

## Slide 37
> 60º
Earth Observing Satellites: Examples

## Slide 38
Earth Observing Satellites: Examples
14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
Click a satellite’s name for the current status. As of January 2023
Key
Year
Launched 1998
Launched 2005
Launched 2011
NOAA-21
Operational satellite extended life estimates (indicated by an arrow) are based on July 2022
reliability analyses (60% confidence) for satellites in orbit for at least one year.
Suomi NPP: Suomi National Polar-orbiting Partnership; JPSS: Joint Polar Satellite System
NOAA-20
NOAA-15 NOAA-18
NOAA-19
Suomi NPP
Launched 2009
JPSS-3
JPSS-4
In-orbit and operational
14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38
Planned mission

## Slide 39
AVHRR- Vis/IR imager
VIIRS - vis/IR imager
CMIS - μwave imager
CrIS - IR sounder
ATMS - μwave sounder
SESS - space environment
GPSOS - GPS occultation
OMPS - ozone
ADCS - data collection
SARSAT - search & rescue
APS - aerosol polarimeter
ERBS - Earth radiation budget
SS - laser sensor
ALT - altimeter
TSIS - solar irradiance
NOAA Satellite Series
Single satellite design with common sensor locations
CMIS
VIIRS
CrIS
ATMS
ERBS
OMPS
Earth Observing Satellites: Examples

## Slide 40: AVHRR
Collecting data since 1978
Currently 6 in orbit (
2 to 15 images a day
Whiskbroom scanning pattern
1.1 km2 resolution
5+ spectral channels
  Infrared - channels 3, 4, 5
  Visible - channels 1, 2
Spacecraft | Mission Operational Status
NOAA 15 | AM Secondary
NOAA 18 | AM Backup
NOAA 19 | PM Primary
NOAA 20 | PM Primary
NOAA Satellite Series
Earth Observing Satellites: Examples

## Slide 41
Instrument: MODIS on board Suomi NPP, Aqua & Terra Satellites
NOAA Satellite Series
Earth Observing Satellites: Examples

## Slide 42
VIIRS on board Suomi NPP and NOAA-20
MODIS and AVHRR successor, high resolution with wide swath
VIIRS swath – 3040km
NOAA Satellite Series
Earth Observing Satellites: Examples

## Slide 43
VIIRS on board Suomi NPP and NOAA-20
MODIS and AVHRR successor, high resolution with a wide swath of 3040 km
NOAA Satellite Series
Earth Observing Satellites: Examples

## Slide 44
Geostationary Orbit Advantages:
large coverage area (about a third of Earth's surface)
High image frequency (Less than 15 minutes) -> enabling monitoring of rapidly-evolving events.
Low Orbiting Vs. Geostationary Satellites

## Slide 45
Geostationary Orbit Limitations:
Polar regions are not observed.
Relatively Low ground spatial resolution. The high orbit imposes a limit of about 1 km at best with current instrument technology.
Low Orbiting Vs. Geostationary Satellites

## Slide 46
Polar Orbit Advantages:
Global coverage.
Good ground resolution because of low orbit.
Low Orbiting Vs. Geostationary Satellites

## Slide 47
Low Orbiting Vs. Geostationary Satellites
Geostationary Satellite
Polar Orbiting Satellite
Tropical Cyclone Shaheen at 09:15 UTC on October 2, 2021. (EUMETSAT/Meteosat-8, RAMMB/CIRA)
Sentinel-3 visible satellite image of Cyclone Shaheen in the Gulf of Oman, approaching landfall west of Muscat, Oman, on October 3, 2021(Copernicus EU)
Notes: Improved spatial resolution – IR
Lili GOES

## Slide 48
Polar Orbit Limitations:
Low image Frequency -> Each point on Earth's surface is observed at best every orbit for polar regions (100 minutes), at worst twice per day for equatorial regions. Multi-satellite systems solve this problem.
Low Orbiting Vs. Geostationary Satellites

## Slide 49
identify the time when the convective cell affected AlAmerat on 15th March 2023
Use an infrared band to see the convective cell. What is the difference between infrared images and visible images?
Practical Task 2
Go to
https://view.eumetsat.int/productviewer?v=default
add layer -> MSG – IODC -> Natural Colour Enhanced RGB

## Slide 50
identify the time when the convective cell affected AlAmerat on 3rd March 2023
Use an infrared band to see the convective cell. What is the difference between infrared images and visible images?
Practical Task 2
Go to
https://view.eumetsat.int/productviewer?v=default
add layer -> MSG – IODC -> Natural Colour Enhanced RGB
Answer : Visible images has texture such as apparent cloud depth and shadows

## Slide 51
For 01/06/2007 12 UTC and 06/06/2007 - add layer -> Sea Surface Temperature (Multi-mission / GHRSST)
- Compare Oman Sea surface Surface Temperature for the two days. Which is higher? What do you think the cause of the difference?
Practical Task 3
Go to https://worldview.earthdata.nasa.gov/

## Slide 52
Future of Earth Observation Satellites

## Slide 53
Future of Earth Observation Satellites
> 60º
New Wave of Satellites
Notes: https://www.esa.int/ESA_Multimedia/Images/2019/05/ESA-developed_Earth_observation_missions https://futureearth.org/publications/explainers/plans-for-a-new-wave-of-european-sentinel-satellites/ https://earth.esa.int/eogateway/catalog

## Slide 54: Meteosat Third Generation Satellites
Twin satellite concept :
4 geostationary imaging satellites (MTG-Imager )
2 geostationary sounding satellites (MTG-Sounder)
MTG-Imager:
- Flexible Combined Imager (FCI) - Improved
- Lightning Imager Instrument (LI) - New
MTG-Sounder:
- Infrared Sounder (IRS) - New
- Ultra-violet, Visible and Near-infrared Sounder (UVN) - New

## Slide 55: Meteosat Third Generation Satellites - Launch plan
SATELLITE | PLANNED LAUNCH DATE | DETAILS
MTG Imager1 | 13 Dec 2022 | Imaging (FCI, LI)
MTG Sounder1 | Q4 2023 | Sounding (IRS, UVN)
MTG Imager2 | Q3 2025 | Imaging (FCI, LI)
MTG Imager3 | Q2 2028 | Imaging (FCI, LI)
MTG Sounder2 | Q4 2030 | Sounding (IRS, UVN)
MTG Imager4 | Q4 2032 | Imaging (FCI, LI)
Flexible Combined Imager (FCI), Lightning Imager (LI), Infrared Sounder (IRS), Copernicus Sentinel-4 ultraviolet visible & near-infrared mission (UVN)
Notes: https://www.eumetsat.int/meteosat-third-generation

## Slide 56
Future of Earth Observation Satellites
New Wave of Satellites
Notes: https://www.esa.int/ESA_Multimedia/Images/2019/05/ESA-developed_Earth_observation_missions https://futureearth.org/publications/explainers/plans-for-a-new-wave-of-european-sentinel-satellites/