## Slide 1: Standard Operating Procedures
OMAN
Civil Aviation Authority
Jaifar Al-Busaidi
Forecaster and TEW Operator
8/2022
المَركز ُالوَطنِي لِلإنذار المُبكِر مِنَ المخَاطِر المتعَددة
National Multi Hazard Early Warning Centre

## Slide 2: Content
Importance of SOP
National Committee for Emergency Management
Civil Aviation Authority and Director general of Meteorology.
  Standard Operation Procedures for Weather
  Standard Operation Procedures for Tsunami.

## Slide 3
Emergency:
Emergencies and crises
Joint Security Operations Committee
Accidents and security crises
National Emergency Management Committee
Disasters / Emergencies
National Security Council
His Majesty the Sultan, the Supreme Commander

## Slide 4
Decisions to adopt the national plan and set up sectors and sub-committees
2018
The Council of Ministers approved the national system in its session No. 17/2015
2015
Royal orders to develop the national system for emergency management
2010
Formation of the National Emergency Committee / National Committee for Natural Disasters
1988
Adoption of the National Disaster Management Plan
2003
Establishment of the Executive Office of the National Civil Defense Committee
2002
The Council of Ministers approved the national system in its session No. 17/2015
2003
2020
Decisions to adopt the national plan and set up sectors and sub-committees
2018
The Council of Ministers approved the national system in its session No. 17/2015
2015
Royal orders to develop the national system for emergency management
2010
Formation of the National Emergency Committee / National Committee for Natural Disasters
1988
Adoption of the National Disaster Management Plan
2003
Establishment of the Executive Office of the National Civil Defense Committee
2002
The Council of Ministers approved the national system in its session No. 17/2015
2003
2020
Royal Decree No. (5/2020) to change the name to the National Committee for the Management of Emergency Situations and the establishment of the National Center for the Management of Emergency.
Ministerial Resolution No. (34/2020) Re-formation of the National Committee For emergency management

## Slide 5: committee concern
It is the committee concerned with managing emergency situations (natural, industrial and environmental) in the Sultanate of Oman. It works according to an integrated system to reduce the effects of emergency situations and major accidents through:
Monitoring risks and early warning about them.
Preparation and readiness.
Emergency response.
Restore and recovery.

## Slide 6
Strengthening and harnessing national capabilities and
resources to provide urgent humanitarian relief
to those affected
Preparing, leading and implementing the national emergency management plan to prevent or mitigate the effects of the emergency
Everything that would protect lives, property and national capabilities during emergency situations
Coordination of national efforts to manage emergency situations (prevention, preparedness, response and recovery)
Function

## Slide 7
National Security Council
National Emergency Management Center
Inspector General of Police and Customs
vice president Assistant Inspector General of Police and Customs for Operations
Public Authority for Water
Civil Aviation Authority
Consumer Protection Agency
Environment Agency
Civil society organizations and institutions
Ministries
Education
Energy and minerals
Social development
Trade, Industry and Investment Promotion
Transport, Communications and Information Technology
Agricultural wealth and fishery water resources
Ministry of Housing and Urban Planning
the health
media
interior
Heritage and Tourism
Finance
Oman Royal Army
Royal Oman Police
Authority of Civil Defense and Ambulance
Military and security agencies
Organizational Chart

## Slide 8
Disaster Risk Reduction
Social and institutional resilience
Enhancing capabilities, ensuring readiness and achieving integration
Goal
Oman is ready
VALUES
PROFESSIONAL PRACTICES
ORGANIZE
PLANNING
COORDINATION
COOPERATE
COMMUNICATE
TRAINING
EXERCISE
INTEGRATION
EXECUTION
Mission
Reducing the risks of emergencies and minimizing their effects
Vision

## Slide 9: Importance of SOP
Scientific progress in the field of forecasting has made it possible to provide unprecedented warnings with their accuracy in a time limit that achieve the objectives of the NMHEWC, contribute to the safety of life and mitigate damage to property.
Weather forecasting enables governments, economic sectors and the public to take appropriate action through information that shows how weather hazards will affect their lives, property and livelihoods.

## Slide 10: Standard Operating Procedures in managing Severe weather cases
Started in 2004 at the DGMET after MAY 2002 Dhofar tropical cyclone.
It showed the steps to issue a general weather warning by the meteorology department.
It included the role of every personal during the times of weather extreme events.
Updated in 2009, 2012, 2016, 2020.
Added some flow charts, criteria, intensity tables, steps, and quality documentation form of ISO 9001/2015.
Added new bulletin samples and some stakeholders reports samples.

## Slide 11: taken Actions in different weather conditions

## Slide 12: Weather parameter classifications according to the colors
Precipitation (mm) 24 hours wind (knot) | < 20 | 30 - 20 | 31- 70 | > 70
<25 | Green | Yellow | Orange | Red
25 - 39 | Yellow | Yellow | Orange | Red
40 - 60 | Orange | Orange | Orange | Red
> 60 | Red | Red | Red | Red
n | Wind Type | Wind Speed
1 | Light wind | 5 – 12 Knots
2 | Moderate winds | 13 – 18 Knots
3 | Active wind | 19 – 24 Knots
4 | Strong wind | 25 – 31 Knots
5 | Very strong winds | 32+ Knots

## Slide 14
Weather SOP
Other extreme weather
n | For weather conditions (winter depressions and local formations) | 
1 | Weather Bulletin | Issued 72 hours before the impact of the case. Renew once every 48 hours (if necessary). Issued by status strength level table A serial number and a release number are given.
2 | Heavy rain alert | Issued at the sharpness level. Renewed once every 24 hours. Issued by status strength level table Gives a serial number and a release number
3 | Tweets for heavy rain in the form of an alert | If there is a possibility of rainfall exceeding 15 mm. The tweet is released 3 hours ago Validity does not exceed one hour.

## Slide 15: Operational Procedures
The Internal Committee for the Management of Exceptional Weather Conditions and its Operational Procedures
Duties of the Exceptional Weather Management Committee
Formation of shift work teams (for other departments)
  Tasks of the first working group (forecasting and early warning)
  Tasks of the second working group (numerical predictions and studies)
  Tasks of the third working group (support operations IT & maintenance)
  Duties of the Director of the Media and Communications Department at CAA.

## Slide 16: Weather Bulletin Samples

## Slide 17: Weather Bulletin Samples

## Slide 18: Weather Alerts and tweets Samples

## Slide 20: Contacts

## Slide 21: Importance of Impact based forecast
The third version of the SOP for the NMHEWC aims in an effort to improve forecasting and early warning services based on impacts, by ensuring the arrival of appropriate information that helps the public and the committees emanating from the National Emergency Management Committee to respond optimally during exceptional weather situations to ensure the main goal in preserving lives and the gains of the homeland and property.

## Slide 22: Weather Impact based Forecast SOP Introduction and goal
Scientific advancement in the field of weather prediction supports predicting risk effects.
The third version of the SOP for the NMHEWC goal is to improve prediction and early warning services based on the Impact of the weather changes.
Provide warnings on time to achieves the purpose of life saving and to reduce the damage to property.
IBF can be used by decision makers in Public and private sectors also by average people to take appropriate measures through the information that shows how the weather threats will affect their lives, properties and ways to live.
Ensuring the arrival of appropriate information that helps the public and National Committee for the Management of Emergency to optimize response.
The ultimate goal is to preserve lives, national gains and property.
This guide shows the necessary steps to deal with weather conditions at the NMHEWC from multiple risks in order to contribute to the safety of life and to reduce damage to property and infrastructure.

## Slide 23: Weather Impact based Forecast SOP The most important modification in the SOP
Prediction according to the potential effect and risks associated with the change of weather.
Reducing construction speech and converting reports to specific points that are updated without changing the formulation.
Separate the level of impact from the status level in the tropics (tropical depression/ tropical cyclone).
Adopting the color schedule in determining the levels of impact .
Reducing a series of approvals and modifications and therefore the information get to all to response to the developments in the weather.
Activating and elevating the NMHEWC role in the management of the weather information.
Facilitating the arrival of the correct information and its absorption from the public and private authorities, institutions and the public.

## Slide 24: Weather Impact based Forecast SOP The idea of the proposed system is based on the classification of the effect of the weather condition
Alarm Level | Alarm level color | Level of impact | Level of general warning response | Potential impact | Recommended action
Level 1 | green | No effect. (Low effect) | No action. | Slight effect No impact on daily activities and routine life. Weather does not pose a life-threatening threat. | 1. Follow daily weather bulletins.
Level 2 | yellow | medium | Be informed. | Slight effect No impact on daily activities and routine life. Weather does not pose a life-threatening threat. | 1. You should stay up to date with updates, weather bulletins and alerts. 2. It is advisable to change the daily routine in accordance with the weather.
Level 3 | orange | High | Be prepared. | Relative or low effect Danger is possible but normal Some public and basic services are likely to be affected The weather is likely not life-threatening. | 1. You should stay up to date with updates, weather bulletins and alerts. 2. Avoid going out and moving during this period. 3. You must change your plans in accordance with the weather. 4. Follow the advice of official emergency management authorities and local authorities.
Level 4 | red | severe | Take precautionary action. | Medium or strong effect Unusual risk potential Infrastructure is likely to be partially damaged and some public and basic services are cut off. Weather can cause a risk to your life if you are directly affected | 1. You should stay up to date with updates, weather bulletins and alerts. 2. Take appropriate action to keep yourself and others safe. 3. Avoid areas likely to be affected by the situation and move to its security areas. 4. Follow the advice of official emergency management authorities and local authorities.

## Slide 25: The graphic plan for the Impact based forecast approach
Weather Impact based Forecast SOP

## Slide 26: Effect levels of weather phenomena
weather phenomena
The severity of the weather
The level of effect
Standards to meet the level of effect
The phenomena that were considered:
  Rain
  Sand and dust storms
  Fog
  Cold wave
  Heat wave
  Sea ​​waves
  Storm surge
Weather Impact based Forecast SOP

## Slide 27
Precipitation (rain)
weather element | Alarm level color | Severity of the weather element | Level of impact | level of impact criteria Amount of rain likely
Rain | green | Light to medium | Low | Less than 20 mm/h (less than 40 mm/24 hours)
Level 2 | yellow | Heavy rains | Medium | 20-30 mm/h (40-60 mm/24 hours)
Level 3 | orange | Very heavy rain. | High | 30-50 mm/h (60-80 mm/24 hours)
Level 4 | Red | Hefty rain | Severe | Above 50 mm/h (or 80 mm/24 h)

## Slide 28
Wind
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria Average wind speed per minute - knot
Wind | green | Light to active | Low | Less than 30
Level 2 | yellow | Active to strong | Medium | 31 - 40
Level 3 | orange | Very strong | High | 41 - 63
Level 4 | Red | Severe | Severe | Above 64

## Slide 29
Sand and Dust Storms
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria horizontal visibility decreasing due to dust
Sand and Dust Storms | green | Dust spread and dust rise | Low | Above 5000 meters
Level 2 | yellow | Medium density | Medium | 3000 - 5000 m
Level 3 | orange | Dense | High | 1000 -3000 m
Level 4 | Red | Very dense | Severe | Less than 1000 meters

## Slide 30
Fog
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria horizontal visibility decreasing due to fog
Fog | green | High humidity | Low | Above 1500 meters
Level 2 | yellow | Average density | Medium | 1000 to 1500 meters
Level 3 | orange | Too dense | High | 500 to 1000 meters
Level 4 | Red | High density | Severe | Less than 500 meters

## Slide 31
Cold Wave
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria Tangible heat
Cold Wave | green | Natural | Low | More than 15°C
Level 2 | yellow | Cold day | Medium | 10 to 15°C
Level 3 | orange | Cold wave | High | 5 to 9°C
Level 4 | Red | Strong cold wave | Severe | Less than 5 degrees Celsius

## Slide 32
Heat Wave
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria Tangible heat
Heat Wave | green | Natural | Low | Less than 37°C
Level 2 | yellow | Hot day | Medium | 37 to 45°C
Level 3 | orange | Heat wave | High | 45 to 50°C
Level 4 | Red | Strong heat wave | Severe | Above 50°C

## Slide 33
Sea waves
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria Wave height
Sea waves | green | quiet | Low | Less than 1.25 meters
Level 2 | yellow | Medium | Medium | 1.5 to 2.5 m
Level 3 | orange | Rough | High | 2.75 to 4 m
Level 4 | Red | Very Rough | Severe | Above 4 m

## Slide 34
D-Storm
weather element | Alarm level color | Severity of the weather element | Level of impact | Level of impact criteria Astronomical tide/wind speed coming from the sea
D-Storm | green | Low | Low | Less than 2.5 meters / less than 50 knots
Level 2 | yellow | Medium | Medium | 2.5 to 3.0 m / 50 - 70 knots
Level 3 | orange | High | High | 3.0 to 3.5 m / 70 - 90 knots
Level 4 | Red | Very High | Severe | 3.0 to 3.5 m / 70 - 90 knots

## Slide 35: The basic operations in monitoring the weather and predicting its impact
A group of tasks in the proposed SOP.
A scheme for the basic daily tasks for weather forecasters.
Appendix to routine tasks lists for each shift period.
Additional tasks for each level.
Activating the management of the weather
cases by forming a team through uniform
alternate schedules.
Activating the internal regulations of the
media dealing at the NMHEWC.
Weather Impact based Forecast SOP
forecast
Impact
forecasting
forecasting
observation
observation
verification
verification

## Slide 36: The plan to deal with the weather conditions at the NMHEWC
Weather Impact based Forecast SOP

## Slide 37: Daily task scheme for NMHEWC Forecaster on duty
Weather Impact based Forecast SOP

## Slide 38: templates
Weather synoptic summary
Weather Impact based Forecast SOP

## Slide 39: templates
Weather Impact based Forecast SOP

## Slide 40: templates
Weather Impact based Forecast SOP

## Slide 41: templates
Weather Impact based Forecast SOP

## Slide 42: The internal regulations for media
Goals of the list
The main organizational regulations of media appearance and social media.
Media dealing levels according to the level of potential impact.
  Green
  Yellow
  Orange
  Red
Weather Impact based Forecast SOP

## Slide 43: The road map to start applying the new SOP
Weather Impact based Forecast SOP
1/DEC
2021
2022
Start work on the renewal and development of the NMHEWC Operational Manual based on IBF
(90% completed)
Complete the work on the guide in the initial structure.
View the guide to alternates and meteorological management to clarify the methodology of the guide, to review and feedback.
Start work on the operational manual of other departments in DGMET.
Encourage employees to take advantage of references and learning tools such as met. ED to understand impact forecasting.
Run the proposed manual for two months by the group's employees in the SOP renewal project
2023
Start the system hopefully
Complete work on the operational manual of other departments in DGMET.
View the guide to the departments in the Civil Aviation Authority to clarify the methodology of the guide.
Work begins on the Operational Guide of the Civil Aviation Authority.
Present the guide to the National Emergency Management Committee and the National Emergency Management Centre to clarify the methodology of the manual.
Work begins on implementation to National Operational Guide.
Modify to NMHEWC manual final structure after the experiment and review.
The manual is partially operated in the center with weather conditions to be able to understand and operate it.
Completion of the operational manual of the departments in DGMET and CAA.
Work on the Salalah Office of Meteorology sub-directory and train its staff as a support NMHEWC in Muscat.
Completion of the updated SOP manual in the National Committee of Emergency Management.
Integration, spacing and redundancy sites in operating chains and updating communication channels.
Start workshops for relevant entities and pilot the system within the National Committee of Emergency Management.
Start broadcasting information through the media and educate the public, citizens and residents in the new bulletins and information (coloring).
Take final approvals for the adoption of the system by warning according to Impact based forecast SOP for weather cases and its operation at the national level in Sultanate of Oman

## Slide 44
Development of meteorological services, accompanying the Oman 2040 vision
Maps for fragility depending on the population density, potentially affected areas and infrastructure.
Run a decision support system (DSS) .
Training technical and administrative cadres associated with operating chains to keep pace with the new system.
Development of the services digitally.
Developing the center studies, updating manuals and improving the procedures periodically to keep pace with the population expansion and increase the building and construction.
Weather Impact based Forecast SOP
Next steps

## Slide 45: Tsunami SOP

## Slide 46
Tsunami SOP
Improvements regarding TEWS
Started in March 2015
The first SOP included 7 different SOP
Updated in 2020 to include only 4 SOP
The updated SOP with implementation of documentation standard ISO 9001/2015
Updating the National Tsunami SOP

## Slide 47
Time line of tsunami warning
Earthquake
T1=5m
T2=6m
0
t5
FIRST WARNING
ESTIMATION OF THE THREAT
FIRST OBSERVATION
END OF THREAT
SECOND OBSERVATION
FIRST UPDATING
SECOND UPDATING
THIRD OBSERVATION
Bulletin no 1
Bulletin no 2
Bulletin no 3.1
Bulletin no 3.2
Bulletin no 3.3
Bulletin no 4
t0
T3=20m
t4
t6
Seismic
Tsunami
scenario
Tide gauge
GPS
Wave radar
Notes: 47
47

## Slide 48
TWS Database
6.5, 7.25, 7.5, 7.75, 8.0, 8.25, 8.5, 8.75, 9.0, 9.25
10 seismic areas considered
10 magnitudes considered
3181 senarios have been caracterizad and modeled to feed the Multihazard Warning system
Sources characterization

## Slide 49
Oman may be affected by
Distant and Local Tsunamis

## Slide 50: Facilities of TWS
Seiscomp3, seismic processing system
TOAST
  Monitoring system
  Easywave for quick tsunami simulation
  Accessing tsunami database
DSS (Dissemination support System)
Tsunami risk maps of 9 cities

## Slide 51
Risk Assessment
National Scale
9 Study Areas at Local Scale

## Slide 52
standard OPERATION PROCEDURE FOR TSUNAMI EARLY WARNING SYSTEM

## Slide 53: Threat map

## Slide 54: Template for TV

## Slide 55
Regional
National
Local
Information
Warning
Official call
for evacuation
TSP
Tsunami
Service
Providers
ONLY FOR DISTANCE TSUNAMI
National
Radio / TV
PUBLIC
Community at risk
NDMO
NTWC
National
Tsunami
Warning
Centre
Feed Back
Tsunami warning National Warning Chain
Near field
25-2-2020
7 Min
8 – 15 Min
ROP
Regional OPS and Local Stations
ROP
DGOPS
PACDA
Civil Defense
& Ambulance
NCCD
National Committee For Civil Defense
National Radio / TV
** Self Evacuation

## Slide 56
Regional
National
Local
Information
Warning
Official call
for evacuation
TSP
Tsunami
Service
Providers
ONLY FOR DISTANCE TSUNAMI
PUBLIC
Community at risk
NTWC
National
Tsunami
Warning
Centre
Feed Back
10 - 30 Min
20 – 60 Min
ROP
Regional OPS and Local Stations
ROP
DGOPS
PACDA
Civil Defense
& Ambulance
NCCD
National Committee For Civil Defense
National Radio / TV
Tsunami warning National Warning Chain
Far field
25-2-2020

## Slide 57
Bulletin 1 (Earthquake info.)
Bulletin 2 (First Tsunami warning)
Bulletin 3 (Tsunami warning update)
Updated Bulletin 3.1 (Tsunami warning update)
Bulletin 4 (Tsunami warning end)
SMS
Email
SMS
Email
FAX
Social Media
SMS
Email
FAX
Social Media
SMS
Email
FAX
Social Media
SMS
Email
FAX
Social Media
Tsunami warning SOP
Public Authority of Television and Radio
Message Number
Communication Method
Expected Action
Time
0-5 Min
5-10
Min
10-30
Min
30-120
Min
2-48
Hours
Wait for Bulletin 2
Podcast Bulletin 2 to start the warning byTV & Radio
Podcast Bulletin 3 by
TV & Radio
Podcast Bulletin 3.1 and the following Bulletins by TV & Radio
Podcast Bulletin 4 to end the warning by TV & Radio

## Slide 58: THANK YOU!
`