## Slide 1: Atmospheric Pressure & Wind
Marine Meteorological Course for Royal Oman Navy
Content creator: Ibrahim Alabdulsalam - Meteorologist
Lecturer: Moza Al Marhoobi - Meteorologist

## Slide 2: Content
1
AIR PRESSURE
Air pressure measurements
High and Low air pressure
2
WIND
Wind speed and Direction
Wind measurements
Forces Governing and Affecting Wind
Sea breeze and land breeze
Monsoon
Wind and Sea Waves
Thunderstorms
Funnel wind

## Slide 3: Subject 1: Air Pressure
Air pressure measurements
High and Low air pressure

## Slide 4: Air Pressure
Pressure is the amount of force acting per unit area.
The symbol of pressure is P
Mathematically:

## Slide 5: Air pressure
Air pressure ,or atmospheric pressure , is the force per unit area exerted on a surface by the weight of air above that surface.

## Slide 6: Air pressure and Density
As the number of air molecules in column of air decreases, the air pressure decreases and vise versa
1013.25mb

## Slide 8: Air pressure and air molecules Air pressure is Equal in all direction

## Slide 9: Pressure and Altitude (Height)

## Slide 10: Experimental examples
جبل شمس صحم
Notes: The air pressure in the bags will likely be the same as the air pressure at the altitude at which they were closed. The ambient air pressure lessens as one rises in altitude. When the air pressure outside the bags is lesser than that inside the bags, like at higher altitude, the air in the bags expands causing the bags to inflate in size.

## Slide 11: Why do my ears pop?
Notes: https://youtu.be/4I9wqVohGOc

## Slide 12: Pressure and Volume

## Slide 13: Pressure and Volume
A gas will expand to fill whatever space it is given.
Thus, if we take a certain amount of gas out of one container and place it into another container that is twice the volume the gas will expand, filling the larger container.
We still have the same number of gas molecules, but now, they are filling as a twice of the volume of the smaller container . Thus, the gas density is halved.
What will be the pressure then?

## Slide 14: Air Pressure Measurements
1.1.
Reading and recording instruments

## Slide 15: Mercury Barometer
The height of the mercury column is a measure of atmospheric pressure.
Pressure Reading

## Slide 16: Aneroid Barometer
Pressure Reading
Notes: An aneroid barometer is an instrument used for measuring air pressure as a method that does not involve liquid. Invented in 1844 by French scientist Lucien Vidi,[21] the aneroid barometer uses a small, flexible metal box called an aneroid cell (capsule), which is made from an alloy of beryllium and copper.

## Slide 17: Recording barograph
continuous records of pressure on a chart paper.
Notes: A barograph is a recording aneroid barometer where the changes in atmospheric pressure are recorded on a paper chart.

## Slide 19: Air pressure units
Inches of mercury (in.Hg).
Millibar (mb).
Hectopascal (hPa).
1 atm = 29.92 in.Hg = 1013.25 hPa = 1013.25 mb
1 hPa = 1 mb

## Slide 20
Why do we need to measure atmospheric pressure?
Notes: To define high and low pressure areas

## Slide 21
High and Low Pressure
Low molecules number / low pressure
1.2.

## Slide 22: Pressure Charts
Pressure chart is drown in one atmospheric level

## Slide 23: Pressure Charts

## Slide 24: Pressure Correction
Notes: 1mb for 10 metres
QFE field elevation (station level)
QNH nautical height (sea level)

## Slide 25: What is the main relationship between air Pressure and Weather?
Notes: Atmospheric pressure is an indicator of weather. When a low-pressure system moves into an area, it usually leads to cloudiness, wind, and precipitation. High-pressure systems usually lead to fair, calm weather.

## Slide 26: Subject 2: Wind
Wind speed and Direction
Wind measurements
Forces Governing and Affecting Wind
Sea breeze and land breeze
Monsoon
Wind and Sea Waves
Thunderstorms
Funnel wind

## Slide 27: Wind
Wind is air in motion.
Wind is the most important relation between air pressure systems and weather.
Wind can be dry, moist, warm and cold etc..
Creates or brings Storms , hurricanes , tornados, wave , dust, cloudiness, clearness , rain and etc..

## Slide 28: What do you think cause wind?

## Slide 29: What do you think cause wind?
Air moves (wind) in response to differences in air pressure.
When there are high- and low-pressure systems, the air will move from higher toward lower pressure.
When it is windy outside, often there is a low-pressure system that air is moving toward.

## Slide 30: Wind speed and Direction
Units of wind speed:
Knot is a nautical mile per hour.
1 Nautical mile = 1852 m =1.852 km
1 mile = 1.6 km
1 knot = 0.51389 m/s
2.1.

## Slide 31: Wind direction is expressed in degrees, From which wind is coming

## Slide 33: Wind in Weather Maps

## Slide 34: Wind Estimation by Satellite

## Slide 35: Wind can be Estimated by Radar

## Slide 36
Cup anemometer (speed)
Wind vane (direction)
Wind Measurement
2.2.

## Slide 37: Upper Air Measurements “Radiosonde”

## Slide 38: Forces Governing and Affecting Wind
Other forces:
  Centripetal force aka Gravity force “GF” “acts toward Earth center”
  Centrifugal force “CentriF” “acts outward from the radius of curvature”
2.3.
Pressure gradient force “PGF”
Always from H to L
CF
90o to the RIGHT in NH and 90o to the LEFT in SH
FF
acts opposite to the wind direction

## Slide 39: The effect of the Coriolis Force
The farther from the equator the object is, the greater the deflection, and the faster an object is moving, the greater the deflection

## Slide 40: Pressure Gradient Force
Which pressure gradient would result in greater wind velocity?
Notes: The pressure gradient force works to move blobs of air from higher pressure toward lower pressure
The gradient wind is a balance of the Pressure Gradient Force, centrifugal and Coriolis. A geostrophic wind becomes a gradient wind when the wind begins flowing through curved height contours. The curving motion introduces a centrifugal (outward fleeing) force

## Slide 41: Geostrophic wind
Gradient wind
Notes: geostrophic wind: a wind whose direction and speed are determined by a balance of the pressure-gradient force and the force due to the earth's rotation.
The gradient wind is a balance of the Pressure Gradient Force, centrifugal and Coriolis. A geostrophic wind becomes a gradient wind when the wind begins flowing through curved height contours. The curving motion introduces a centrifugal (outward fleeing) force

## Slide 42: High, low and Wind Flow

## Slide 43
Northern Hemisphere
Southern Hemisphere

## Slide 44: Convergence and Divergence

## Slide 45: Global distribution of pressure systems “winter”

## Slide 46: Global distribution of pressure systems “summer”

## Slide 47: Sea Breeze and Land Breeze
Sea breeze
Land breeze
2.4.

## Slide 49
Monsoon
9/6/2022
Moza Al Marhoobi
49
Summer Monsoon
Winter Monsoon
2.5.

## Slide 50: Wind and Sea Wave
What’s the relationship between wind and sea waves?
  Direct (the stronger the wind, the higher the waves)
2.6.

## Slide 51: Thunderstorm
Cumulonimbus/anvil
Heavy rain/wind/hail
All downdraft
Light rain/weak winds
All updraft
No rain/wind yet
2.7.
Thunderstorm Stages

## Slide 52: Up and Down draft

## Slide 53
Haboob
Mammatus
Outflow boundary

## Slide 54: FUNNEL EFFECT
2.8.
Notes: the phenomenon where winds will tend to increase in speed as they squeeze through narrow valleys

## Slide 55
Kindly scan this “QR code” to evaluate this lecture.
Thank You!
Scan this please