## Slide 1
Principles of Weather Satellite
Zamzam AL.Rawahi
Zamzam.Rawahi@caa.gov.om
Regional Satellite Application Course for MENA Region / SAC-21
Feb,2026

## Slide 2
From Online-Phase...
The Slido app must be installed on every computer you’re presenting from
Do not edit How to change the design

## Slide 3
Earth Observation Weather Satellite

## Slide 4
Common Orbit Types
Geostationary Orbit
Polar Orbit / Low orbiting

## Slide 5
Common Orbit Types
EUMETSAT currently operates:
MSG (0° longitude): Best Coverage over Africa/Europe, degraded view over India and Brazil.
MSG-IODC (~41.5°E): Best over the Indian Ocean and the Middle East, weaker over western Africa.
MTG (0° longitude, 1 km at nadir): Excellent resolution over Africa/Europe,

## Slide 6
Energy Source (Type of Sensor)
Meteosat-8 41.5⁰ East
Satellites carry sensors or instruments. The names of sensors are usually acronyms that can
include the name of the satellite

## Slide 7
Energy Source (Type of Sensor)
Meteosat-8 41.5⁰ East

## Slide 8
Passive Instruments:
Receives and measures naturally emitted or scattered radiation from the earth and its atmosphere

## Slide 9
Active Instruments:
Like a radar where instrument transmits its own radiation and then collects the reflected or scattered back signals from the earth and its atmosphere

## Slide 10
Expect Spectral ?
Resolution
Spatial
Temporal
Spectral
Radiometric

## Slide 11
Satellite Characteristics/Spatial Resolution
• Pixel – the Smallest Unit of an Image
• Spatial resolution is defined by the size of a pixe1
MSG-0
MTG

## Slide 12
Low Orbiting Vs. Geostationary Satellites
Geostationary Satellite
Polar Orbiting Satellite
Notice the more detailed image from Polar (low orbiting satellite )

## Slide 13
Spatial Resolution

## Slide 14
MSG (SEVIRI) VS MTG (FCI)
Meteosat-8 41.5⁰ East

## Slide 15
Radiometric Resolution
0
255
The ability of a sensor to detect small differences in radiance (number of gray levels per pixel).

## Slide 16
Temporal Resolution
• The time it takes for a satellite to complete one orbit cycle—also called “revisit time”
• It mostly depends on swath width of the satellite – the larger the swath – the higher the temporal resolution
< 10 min
2 times per day

## Slide 17
Temporal Resolution
• The time it takes for a satellite to complete one orbit cycle—also called “revisit time”
• It mostly depends on swath width of the satellite – the larger the swath – the higher the temporal resolution
Geostationary
MODIS (2330)
VIIRS / 3040km
CALIPSO

## Slide 18
Spectral Resolution
Resolution depends upon satellite orbit configuration and sensor design. Different sensors have different resolutions.
Signifies the number and width of spectral bands of the sensor. The higher the spectral resolution, the
narrower the wavelength range for a given channel or band.
More and finer spectral channels enable remote sensing of different parts of the Earth’s surface.
Typically, multispectral imagery refers to 3 to 10 bands, while hyperspectral imagery consists of hundreds or thousands of (narrower) bands (i.e., higher spectral resolution).
Panchromatic is a single broad band that collects a wide range of wavelengths

## Slide 19
Geostationary Satellite
Meteosat-8 41.5⁰ East
large coverage area (about a third of Earth's surface)
High image frequency (every 15 minutes or less )
-> monitoring of rapidly-changing weather and phenomena .
Polar regions are not well observed.
Relatively Low spatial resolution.

## Slide 20
Geostationary Satellite
Meteosat-8 41.5⁰ East
Global coverage.
Good spatial resolution because of low orbit.
low image frequency (2 images a day per satellite )
Swath
Highest Spatial Resolution at the middle of the Swath

## Slide 21
MSG (SEVIRI) VS MTG (FCI)
Meteosat-8 41.5⁰ East
1. Higher Spatial Resolution:
3.8 um and 10.5 um in 2.0 km resolution ( and 1 km in Hi-Re mode)
0.6 um and 2.3 um in 1.0 km resolution ( and 0.5 km in Hi-Re mode)
2. Higher Temporal Resolution
10min and 5min for Rapid Scan
3. Higher Spectral Resolution
16 channels more
4. Higher Radiometric Resolution
MSG SEVIRI has 10-bit resolution (~1024 levels),
while MTG FCI has 12-bit resolution (~4096 levels).

## Slide 22
Credit: https://tinyurl.com/HEISatelliteWorkshop
Electromagnetic radiation: Sun , Earth’s Atmosphere and Surface
Average Global Temperature
15 C

## Slide 23
From photons to products
MTG-I1
MTG-S1

## Slide 24
Satellite Data Processing

## Slide 25
What is really measured?

## Slide 26: Single Channels
Reflected solar radiation
Available during daytime only.
Cloud monitoring
In 0.8 μm vegetation reflects much more used for land an vegetation products

## Slide 27: Single Channel (Enhanced IR10.8)

## Slide 28: Sandwich Products

## Slide 29: Except spectral?
Spatial
Temporal
Spectral
Radiometric
Resolution :

## Slide 30
Spectral Resolution :
Signifies the number and width of spectral bands of the sensor. The higher the spectral resolution, the narrower the wavelength range for a given channel or band.

## Slide 31: Spectral Resolution
3=VIS0.6
4=VIS0.8
7=NIR1.6
10=WV6.2
11=WV7.3
12=IR8.7
13=IR9.7
14=IR10.5
15=IR12.3
16=IR13.3
1=VIS0.4
2=VIS0.5
5=NIR0.9
6=NIR1.3
8=NIR2.25
9=IR3.8
Solar
3.0 (1.0/0.5) km
Thermal
3.0 (2.0/1.0) km

## Slide 32
Spatial Resolution
Spatial Resolution Comparison
MSG-0
MTG

## Slide 33
Spatial Resolution (FCI vs SEVIRI
3km
1km
0.5km
0.6 um and 2.3 um in 1.0 km resolution ( and 0.5 km in Hi-Re mode)
3.8 um and 10.5 um in 2.0 km resolution ( and 1 km in Hi-Re mode)
2km
What’s new? – High Resolution Mode:

## Slide 34
Spatial Resolution

## Slide 35
Parallax Shift :

## Slide 37
Parallax Shift :

## Slide 39
Limb View :
Meteosat 9
Meteosat 10
Meteosat 9
Meteosat 10

## Slide 40
Radiometric resolution :
The ability of a sensor to detect small differences in radiance (number of gray levels per pixel).
MSG SEVIRI has 10-bit resolution (~1024 levels),
while MTG FCI has 12-bit resolution (~4096 levels).
0
255

## Slide 41
Temporal resolution :

## Slide 42
Satellite Data Processing

## Slide 43
Satellite Data Processing

## Slide 44
What is really measured??
Every Object has a temperature > 0 K and should should emit EM.
EMW can be :
Emitted Scattered Reflected Transmitted Absorbed
.
.

## Slide 45
10.8 um sensor
Cold Surface
Hot Surface
Less radiation Intensity \
smaller number of photons
Higher radiation Intensity \
larger number of photons
45 C
-70 C

## Slide 46
Credit: https://tinyurl.com/HEISatelliteWorkshop
Electromagnetic radiation: From Sun , Earth’s Atmosphere and other earth Systems and from Everywhere in the Space
Average Global Temperature
15 C
Cosmic background radiation

## Slide 47
02
What is really measured??

## Slide 48
Data Exploration ?
How to use data??
Single Channels
Channel difference/ratio
Sandwich products
RGB products
L2(+) / Geophysical products

## Slide 49
Single Channels
Reflected solar radiation
In 0.8 μm vegetation reflects much more used for land an vegetation products

## Slide 50
Single Channels (Enhanced IR10.8)

## Slide 51
Sandwich Products

## Slide 52
Cloud top Feature Identification
-90 C
45 C
-70 C
45 C
45 C
-70 C
0.6 um \ Reflectance
Color enhancement of single channels

## Slide 53
RGB Composite !

## Slide 54
Single Channel
Convective Cloud
?
?
?
?
?
?
?
?
?

## Slide 55
Single Channel

## Slide 56
How is RGB image (or RGB composite) made ?
Every spectral channel could be assigned to one of the RGB primary components
Red
Green
Blue
Allows analysis of 3 (or more) spectral characteristics in one image!

## Slide 57
 | R | G | B
 | 255 | 255 | 255
 | 255 | 255 | 0
 | 255 | 0 | 255
 | 0 | 255 | 255
 | 0 | 0 | 0
 | 143 | 143 | 143
 | 255 | 0 | 0
 | 0 | 255 | 0
 | 0 | 0 | 255
Channel’s Intensity
Natural Color RGB

## Slide 60
Ice Cloud
Water cloud
Dust

## Slide 61
Thanks